## Slide 1: ROS – Lecture 11
Lecturer: Roi Yehoshua
roiyeho@gmail.com
October 2016
Behavior-Based Robotics
Where to go next?

## Slide 2: Agenda
Behavior-based robotics
Decision making in ROS
Where to go next?

## Slide 3: Behavior-Based Robotics
The world is fundamentally unknown and changing
Does not make sense to over-plan
Key idea: to develop a library of useful behaviors (controllers)
Switch among behaviors in response to environmental changes

## Slide 4: Behavior
A behavior is a mapping of sensory inputs to a pattern of motor actions
Composed of:
  Start conditions (preconditions) - what must be true to be executable
  Actions - what changes once behavior executes
  Stop conditions - when the behavior terminates

## Slide 5: Behaviors
Behaviors are independent and operate concurrently
  One behavior does not know what another behavior is doing or perceiving
The overall behavior of the robot is emergent
  There is no explicit “controller” module which determines what will be done

## Slide 6: Example: Navigation
Problem: Go to a goal location without bumping into obstacles
Need at least two behaviors: Go-to-goal and Avoid-obstacles

## Slide 7: Behaviors
Avoid object
Wander
Explore
Map
Monitor change
Identify objects
Plan changes

## Slide 8: Behavior-Based Example
Create a new package gazebo_random_walk
Create a launch subdirectory within the package and add the following launch file to it
  $ cd ~/catkin_ws/src
  $ catkin_create_pkg behavior_based std_msgs rospy roscpp

## Slide 9: Behavior Class – Header File
#include <vector>
using namespace std;
class Behavior {
private:
vector<Behavior *> _nextBehaviors;
public:
Behavior();
virtual bool startCond() = 0;
virtual bool stopCond() = 0;
virtual void action() = 0;
Behavior *addNext(Behavior *beh);
Behavior *selectNext();
virtual ~Behavior();
};

## Slide 10: Behavior Class – cpp File
#include "Behavior.h"
#include <iostream>
Behavior::Behavior() {
}
Behavior::~Behavior() {
}
Behavior *Behavior::addNext(Behavior *beh) {
_nextBehaviors.push_back(beh);
return this;
}
Behavior *Behavior::selectNext() {
for (int i = 0; i < _nextBehaviors.size(); i++)
{
if (_nextBehaviors[i]->startCond())
return _nextBehaviors[i];
}
return NULL;
}

## Slide 11: MoveForward Behavior - Header
#include "Behavior.h"
#include <ros/ros.h>
#include "sensor_msgs/LaserScan.h"
#include <cmath>
class MoveForward: public Behavior {
public:
MoveForward();
virtual bool startCond();
virtual void action();
virtual bool stopCond();
virtual ~MoveForward();
private:
const static double FORWARD_SPEED_MPS = 0.5;
const static double MIN_SCAN_ANGLE_RAD = -30.0/180 * M_PI;
const static double MAX_SCAN_ANGLE_RAD = +30.0/180 * M_PI;
const static float MIN_PROXIMITY_RANGE_M = 0.5;
ros::NodeHandle node;
ros::Publisher commandPub;
ros::Subscriber laserSub;
void scanCallback(const sensor_msgs::LaserScan::ConstPtr& scan);
bool keepMovingForward;
};

## Slide 12: MoveForward Behavior – cpp (1)
#include "MoveForward.h"
#include "geometry_msgs/Twist.h"
MoveForward::MoveForward() {
commandPub = node.advertise<geometry_msgs::Twist>("cmd_vel", 10);
laserSub = node.subscribe("base_scan", 1, &MoveForward::scanCallback, this);
keepMovingForward = true;
}
bool MoveForward::startCond() {
return keepMovingForward;
}
void MoveForward::action() {
geometry_msgs::Twist msg;
msg.linear.x = FORWARD_SPEED_MPS;
commandPub.publish(msg);
ROS_INFO("Moving forward");
}
bool MoveForward::stopCond() {
return !keepMovingForward;
}

## Slide 13: MoveForward Behavior – cpp (2)
void MoveForward::scanCallback(const sensor_msgs::LaserScan::ConstPtr& scan)
{
// Find the closest range between the defined minimum and maximum angles
int minIndex = ceil((MIN_SCAN_ANGLE_RAD - scan->angle_min) / scan->angle_increment);
int maxIndex = floor((MAX_SCAN_ANGLE_RAD - scan->angle_min) / scan->angle_increment);
float closestRange = scan->ranges[minIndex];
for (int currIndex = minIndex + 1; currIndex <= maxIndex; currIndex++) {
if (scan->ranges[currIndex] < closestRange) {
closestRange = scan->ranges[currIndex];
}
}
if (closestRange < MIN_PROXIMITY_RANGE_M) {
keepMovingForward = false;
} else {
keepMovingForward = true;
}
}
MoveForward::~MoveForward() {
}

## Slide 14: TurnLeft Behavior - Header
#include "Behavior.h"
#include <ros/ros.h>
#include "sensor_msgs/LaserScan.h"
#include <cmath>
class TurnLeft: public Behavior {
public:
TurnLeft();
virtual bool startCond();
virtual void action();
virtual bool stopCond();
virtual ~TurnLeft();
private:
const static double TURN_SPEED_MPS = 1.0;
const static double MIN_SCAN_ANGLE_RAD = -30.0/180 * M_PI;
const static double MAX_SCAN_ANGLE_RAD = 0;
const static float MIN_PROXIMITY_RANGE_M = 0.5;
ros::NodeHandle node;
ros::Publisher commandPub;
ros::Subscriber laserSub;
void scanCallback(const sensor_msgs::LaserScan::ConstPtr& scan);
bool keepTurningLeft;
};

## Slide 15: TurnLeft Behavior – cpp (1)
#include "TurnLeft.h"
#include "geometry_msgs/Twist.h"
TurnLeft::TurnLeft() {
commandPub = node.advertise<geometry_msgs::Twist>("cmd_vel", 10);
laserSub = node.subscribe("base_scan", 1, &TurnLeft::scanCallback, this);
keepTurningLeft = true;
}
bool TurnLeft::startCond() {
return keepTurningLeft;
}
void TurnLeft::action() {
geometry_msgs::Twist msg;
msg.angular.z = TURN_SPEED_MPS;
commandPub.publish(msg);
ROS_INFO("Turning left");
}
bool TurnLeft::stopCond() {
return !keepTurningLeft;
}

## Slide 16: TurnLeft Behavior – cpp (2)
void TurnLeft::scanCallback(const sensor_msgs::LaserScan::ConstPtr& scan)
{
// Find the closest range between the defined minimum and maximum angles
int minIndex = ceil((MIN_SCAN_ANGLE_RAD - scan->angle_min) / scan->angle_increment);
int maxIndex = floor((MAX_SCAN_ANGLE_RAD - scan->angle_min) / scan->angle_increment);
float closestRange = scan->ranges[minIndex];
for (int currIndex = minIndex + 1; currIndex <= maxIndex; currIndex++) {
if (scan->ranges[currIndex] < closestRange) {
closestRange = scan->ranges[currIndex];
}
}
if (closestRange < MIN_PROXIMITY_RANGE_M) {
keepTurningLeft = true;
} else {
keepTurningLeft = false;
}
}
TurnLeft::~TurnLeft() {
}

## Slide 17: Behavior-Based Robotics
Two main challenges in behavior-based robotics
Behavior selection - How do we select the correct behavior?
Behavior fusion – if several behaviors run in parallel:
  How to merge the results?
  How to determine weight of each behavior in the result?

## Slide 18: State-Based Selection
Every state represents a behavior
Transitions are triggered by sensor readings
Start
A
A
B
C
A
C
A
D
C

## Slide 19: Example: Robot Soccer

## Slide 20: Plan Class – Header file
#include <vector>
#include "Behavior.h"
using namespace std;
class Plan {
public:
Plan();
Behavior *getStartBehavior();
virtual ~Plan();
protected:
vector<Behavior *> behaviors;
Behavior *startBehavior;
};

## Slide 21: Plan Class – cpp File
#include "Plan.h"
#include <iostream>
Plan::Plan() : startBehavior(NULL) {
}
Behavior *Plan::getStartBehavior() {
return startBehavior;
}
Plan::~Plan() {
}

## Slide 22: ObstacleAvoidPlan – Header File
#include "Plan.h"
class ObstacleAvoidPlan: public Plan {
public:
ObstacleAvoidPlan();
virtual ~ObstacleAvoidPlan();
};

## Slide 23: ObstacleAvoidPlan – cpp File
#include "ObstacleAvoidPlan.h"
#include "MoveForward.h"
#include "TurnLeft.h"
#include "TurnRight.h"
ObstacleAvoidPlan::ObstacleAvoidPlan() {
// Creating behaviors
behaviors.push_back(new MoveForward());
behaviors.push_back(new TurnLeft());
behaviors.push_back(new TurnRight());
// Connecting behaviors
behaviors[0]->addNext(behaviors[1]);
behaviors[0]->addNext(behaviors[2]);
behaviors[1]->addNext(behaviors[0]);
behaviors[2]->addNext(behaviors[0]);
startBehavior = behaviors[0];
}

## Slide 24: Manager – Header File
#include "Plan.h"
#include "Behavior.h"
class Manager {
public:
Manager(Plan *plan);
void run();
virtual ~Manager();
private:
Plan *plan;
Behavior *currBehavior;
};

## Slide 25: Manager – cpp File
#include "Manager.h"
#include <ros/ros.h>
Manager::Manager(Plan *plan) : plan(plan) {
currBehavior = plan->getStartBehavior();
}
void Manager::run()
{
ros::Rate rate(10);
if (!currBehavior->startCond()) {
ROS_ERROR("Cannot start the first behavior");
return;
}
while (ros::ok() && currBehavior != NULL) {
currBehavior->action();
if (currBehavior->stopCond()) {
currBehavior = currBehavior->selectNext();
}
ros::spinOnce();
rate.sleep();
}
ROS_INFO("Manager stopped");
}

## Slide 26: Run.cpp
#include "Manager.h"
#include "ObstacleAvoidPlan.h"
#include <ros/ros.h>
int main(int argc, char **argv) {
ros::init(argc, argv, "behavior_based_wanderer");
ObstacleAvoidPlan plan;
Manager manager(&plan);
// Start the movement
manager.run();
return 0;
};

## Slide 27: Behavior-Based Example
Create a launch subdirectory within the package and copy the launch file from gazebo_random_walk package
Change the following lines in the launch file

## Slide 28: behavior_based_wanderer.launch
<launch>
<param name="/use_sim_time" value="true" />
<!-- Launch world -->
<include file="$(find gazebo_ros)/launch/willowgarage_world.launch"/>
<arg name="init_pose" value="-x -5 -y -2 -z 1"/>
<param name="robot_description" textfile="$(find r2d2_description)/urdf/r2d2.urdf"/>
<!-- Spawn robot's model -->
<node name="spawn_urdf" pkg="gazebo_ros" type="spawn_model" args="$(arg init_pose) -urdf -param robot_description -model my_robot" output="screen"/>
<node name="joint_state_publisher" pkg="joint_state_publisher" type="joint_state_publisher"/>
<node pkg="robot_state_publisher" type="robot_state_publisher" name="robot_state_publisher" output="screen"/>
<!-- Launch random walk node -->
<node name="behavior_based_wanderer" pkg="behavior_based" type="behavior_based_wanderer" output="screen"/>
</launch>

## Slide 29: Behavior-Based Example

## Slide 30: Decision Making in ROS
http://wiki.ros.org/decision_making
Light-weight, generic and extendable tools for writing, executing, debugging and monitoring decision making models through ROS standard tools
Supports different decision making models:
  Finite State Machines
  Hierarchical FSMs
  Behavior Trees
  BDI
Developed by Cogniteam

## Slide 31: Where To Go Next?
There are still many areas of ROS to explore:
  3-D image processing using PCL
  Identifying your friends and family using face_recognition
  Identifying and grasping objects on a table top
    or how about playing chess?
  Building knowledge bases with knowrob
  Learning from experience using reinforcement_learning

## Slide 32: Where To Go Next?
There are now over 2000 packages and libraries available for ROS
Click on the Browse Software link at the top of the ROS Wiki for a list of all ROS packages and stacks that have been submitted for indexing.
When you are ready, you can contribute your own package(s) back to the ROS community
Welcome to the future of robotics.
Have fun and good luck!