## Slide 1: ROS – Lecture 8
Lecturer: Roi Yehoshua
roiyeho@gmail.com
October 2016
ROS actions
Sending goal commands from code
Making navigation plans

## Slide 2: Actions
http://wiki.ros.org/actionlib
While services are handy for simple get/set interactions like querying status and managing configuration, they don’t work well with long-running tasks
  such as sending a robot to some distant location
ROS actions are the best way to implement interfaces to time-extended, goal-oriented behaviors
Similar to the request and response of a service, an action uses a goal to initiate a behavior and sends a result when the behavior is complete
But the action further uses feedback to provide updates on the behavior’s progress toward the goal and also allows for goals to be canceled
Actions are asynchronous (in contrast to services)

## Slide 3: Action Client-Server Interaction

## Slide 4: Action Server State Transitions

## Slide 5: Action Client State Transitions

## Slide 6: .action File
The action specification is defined in an .action file
  These files are placed in the package’s ./action directory
Example for an action file:

## Slide 7: .action File
From the action file the following message types are generated:
  DoDishesAction.msg
  DoDishesActionGoal.msg
  DoDishesActionResult.msg
  DoDishesActionFeedback.msg
  DoDishesGoal.msg
  DoDishesResult.msg
  DoDishesFeedback.msg
These messages are then used internally by actionlib to communicate between the ActionClient and ActionServer

## Slide 8: SimpleActionClient
A simple client implementation which supports only one goal at a time
The action client is templated on the action definition, specifying what message types to communicate to the action server with
The action client c’tor also takes two arguments:
  The server name to connect to
  A boolean option to automatically spin a thread
    If you prefer not to use threads (and you want actionlib to do the 'thread magic' behind the scenes), this is a good option for you.

## Slide 9: SimpleActionClient

## Slide 10: SendGoals
The next code is a simple example to send a goal to move the robot from the C++ code
In this case the goal would be a PoseStamped message that contains information about where the robot should move to in the world
http://wiki.ros.org/navigation/Tutorials/SendingSimpleGoals

## Slide 11: SendGoals
First create a new package called send_goals
This package depends on the following packages:
  actionlib
  geometry_msgs
  move_base_msgs
  $ cd ~/catkin_ws/src
  $ catkin_create_pkg send_goals std_msgs rospy roscpp actionlib tf geometry_msgs move_base_msgs

## Slide 12: SendGoals
Open the project file in Eclipse
Under the src subdirectory, create a new file called SendGoals.cpp

## Slide 13: SendGoals.cpp (1)
#include <ros/ros.h>
#include <move_base_msgs/MoveBaseAction.h>
#include <actionlib/client/simple_action_client.h>
#include <tf/transform_datatypes.h>
typedef actionlib::SimpleActionClient<move_base_msgs::MoveBaseAction> MoveBaseClient;
int main(int argc, char** argv) {
ros::init(argc, argv, "send_goals_node");
// Get the goal's x, y and angle from the launch file
double x, y, theta;
ros::NodeHandle nh;
nh.getParam("goal_x", x);
nh.getParam("goal_y", y);
nh.getParam("goal_theta", theta);
// create the action client
MoveBaseClient ac("move_base", true);
// Wait 60 seconds for the action server to become available
ROS_INFO("Waiting for the move_base action server");
ac.waitForServer(ros::Duration(60));
ROS_INFO("Connected to move base server");

## Slide 14: SendGoals.cpp (2)
// Send a goal to move_base
move_base_msgs::MoveBaseGoal goal;
goal.target_pose.header.frame_id = "map";
goal.target_pose.header.stamp = ros::Time::now();
goal.target_pose.pose.position.x = x;
goal.target_pose.pose.position.y = y;
// Convert the Euler angle to quaternion
double radians = theta * (M_PI/180);
tf::Quaternion quaternion;
quaternion = tf::createQuaternionFromYaw(radians);
geometry_msgs::Quaternion qMsg;
tf::quaternionTFToMsg(quaternion, qMsg);
goal.target_pose.pose.orientation = qMsg;
// Send the goal command
ROS_INFO("Sending robot to: x = %f, y = %f, theta = %f", x, y, theta);
ac.sendGoal(goal);

## Slide 15: SendGoals.cpp (3)
// Wait for the action to return
ac.waitForResult();
if (ac.getState() == actionlib::SimpleClientGoalState::SUCCEEDED)
ROS_INFO("You have reached the goal!");
else
ROS_INFO("The base failed for some reason");
return 0;
}

## Slide 16: Converting Euler Angle to Quaternion
It is easier to define the goal pose with Euler angles rather than with quaternions
The following code translates the angle from radians to quaternion representation:
double theta = 90.0;
double radians = theta * (M_PI/180);
tf::Quaternion quaternion;
quaternion = tf::createQuaternionFromYaw(radians);
geometry_msgs::Quaternion qMsg;
tf::quaternionTFToMsg(quaternion, qMsg);
goal.target_pose.pose.orientation = qMsg;

## Slide 17: SendGoals Launch File
  <launch>
  <param name="goal_x" value="2" />
  <param name="goal_y" value="-2" />
  <param name="goal_theta" value="180" />
  <param name="/use_sim_time" value="true"/>
  <!-- Launch turtle bot world -->
  <include file="$(find turtlebot_gazebo)/launch/turtlebot_world.launch"/>
  <!-- Launch navigation stack with amcl -->
  <include file="$(find turtlebot_gazebo)/launch/amcl_demo.launch"/>
  <!-- Launch rviz -->
  <include file="$(find turtlebot_rviz_launchers)/launch/view_navigation.launch"/>
  <!-- Launch send goals node -->
  <node name="send_goals_node" pkg="send_goals" type="send_goals_node" output="screen"/>
  </launch>

## Slide 18: SendGoals Demo
Launch send_goals.launch:
You should now see rviz opens and the robot moves from its initial pose to the target pose defined in the launch file
$ roslaunch send_goals send_goals.launch

## Slide 19: SendGoals Demo

## Slide 20: SendGoals Demo

## Slide 21: SendGoals Demo

## Slide 22: Nodes Graph

## Slide 23: make_plan service
Allows an external user to ask from move_base a route to a given pose
  without actually moving the robot
Arguments:
  Start pose
  Goal pose
  Goal tolerance
Returns a message of type nav_msgs/GetPlan

## Slide 24: make_plan Node
In our send_goal package we will now create a make_plan_node that will call the make_plan service and print the output path of the plan
Add a new C++ file called MakePlan.cpp

## Slide 25: MakePlan.cpp (1)
#include <ros/ros.h>
#include <nav_msgs/GetPlan.h>
#include <geometry_msgs/PoseStamped.h>
#include <string>
using std::string;
#include <boost/foreach.hpp>
#define forEach BOOST_FOREACH
double goalTolerance = 0.5;
void fillPathRequest(nav_msgs::GetPlan::Request &req);
void callPlanningService(ros::ServiceClient &serviceClient, nav_msgs::GetPlan &srv);

## Slide 26: MakePlan.cpp (2)
int main(int argc, char** argv)
{
ros::init(argc, argv, "make_plan_node");
ros::NodeHandle nh;
// Init service query for make plan
string service_name = "move_base/make_plan";
while (!ros::service::waitForService(service_name, ros::Duration(3.0))) {
ROS_INFO("Waiting for service move_base/make_plan to become available");
}
ros::ServiceClient serviceClient = nh.serviceClient<nav_msgs::GetPlan>(service_name, true);
if (!serviceClient) {
ROS_FATAL("Could not initialize get plan service from %s", serviceClient.getService().c_str());
return -1;
}
nav_msgs::GetPlan srv;
fillPathRequest(srv.request);
if (!serviceClient) {
ROS_FATAL("Persistent service connection to %s failed", serviceClient.getService().c_str());
return -1;
}
callPlanningService(serviceClient, srv);
}

## Slide 27: MakePlan.cpp (3)
void fillPathRequest(nav_msgs::GetPlan::Request &request)
{
request.start.header.frame_id = "map";
request.start.pose.position.x = 0;
request.start.pose.position.y = 0;
request.start.pose.orientation.w = 1.0;
request.goal.header.frame_id = "map";
request.goal.pose.position.x = 2.0;
request.goal.pose.position.y = -2.0;
request.goal.pose.orientation.w = 1.0;
request.tolerance = goalTolerance;
}

## Slide 28: MakePlan.cpp (4)
void callPlanningService(ros::ServiceClient &serviceClient, nav_msgs::GetPlan &srv)
{
// Perform the actual path planner call
if (serviceClient.call(srv)) {
if (!srv.response.plan.poses.empty()) {
forEach(const geometry_msgs::PoseStamped &p, srv.response.plan.poses) {
ROS_INFO("x = %f, y = %f", p.pose.position.x, p.pose.position.y);
}
}
else {
ROS_WARN("Got empty plan");
}
}
else {
ROS_ERROR("Failed to call service %s - is the robot moving?", serviceClient.getService().c_str());
}
}

## Slide 29: make_plan.launch
<launch>
<param name="goal_x" value="2" />
<param name="goal_y" value="-2" />
<param name="goal_theta" value="180" />
<param name="/use_sim_time" value="true"/>
<!-- Launch turtle bot world -->
<include file="$(find turtlebot_gazebo)/launch/turtlebot_world.launch"/>
<!-- Launch navigation stack with amcl -->
<include file="$(find turtlebot_gazebo)/launch/amcl_demo.launch"/>
<!-- Launch send goals node -->
<node name="make_plan_node" pkg="send_goals" type="make_plan_node" output="screen"/>
</launch>

## Slide 30: Running make_plan Node